## Slide 1
IOT & ROBOTICS | MAJOR PROJECT
SMART ATTENDANCE SYSTEM USING RFID
ESP32 • RC522 RFID • 16x2 I2C LCD LED and buzzer feedback
PROJECT DOCUMENTATION
Source code, circuit and test results
Prototype photograph supplied by project team

## Slide 2
Problem Statement & Aim
Why an RFID-based approach is useful
2
Problem
Manual attendance can take time and can lead to recording errors. Maintaining consistent and easily retrievable attendance records can be difficult with purely manual methods.
Project aim
Build a small prototype that reads an RFID card, checks whether its UID is registered, and provides immediate LCD, LED, buzzer, and Serial Monitor feedback.
RFID helps automate card identification; a card UID alone does not prove the cardholder's identity.

## Slide 3
Objectives
Functions implemented in the supplied firmware
3
Read RC522 cards through SPI on the ESP32.
Map registered card UIDs to student names.
Store student registrations in ESP32 Preferences.
Show prompts and status messages on a 16x2 LCD.
Use red/green LEDs and a buzzer for feedback.
Prevent a second attendance mark for the same UID during the current power session.
Physical assembly documented in the supplied photo.

## Slide 4
Hardware Components
Components used in the completed and tested prototype
4
ESP32
Controller and program storage.
RC522 RFID
Reads a compatible card/tag UID.
16x2 I2C LCD
Local prompts and result messages.
Green + red LEDs
Visual feedback through 220 Ω resistors.
Buzzer module
Provides audible feedback for scan results.
Breadboard + wires
Prototyping interconnections.

## Slide 5
System Architecture
Data and control flow
5
RFID Card
UID presented
RC522
Reads card UID
ESP32
Checks registration and duplicate state
Outputs
LCD + LEDs + buzzer
Serial Monitor
Status / event log
Persistent data
Registered UID/name mappings stored using ESP32 Preferences.
Session data
Attendance de-duplication is in RAM and resets after power cycle.

## Slide 6
Circuit Design & Pin Mapping
Pin mapping used in the tested prototype
6
Safety: RC522 uses 3.3V; ensure LCD I2C signals are 3.3V-safe; confirm buzzer pinout.

## Slide 7
Working Principle
Card scan decision flow
7
1. Startup
Initialize Serial, GPIO, LCD, SPI and RC522.
2. Load records
Read registered student UID/name pairs from Preferences.
3. Scan card
Read and normalize the RFID UID.
4. Check UID
Unknown UID -> red LED and not-registered message.
5. Check duplicate
Already marked this session -> already-marked message.
6. Mark attendance
Registered, not yet marked -> green LED, name message and success beep.

## Slide 8
Software Features & Serial Commands
Open Serial Monitor at 115200 baud; select Newline as line ending
8
Command | Purpose
HELP | Shows command list and usage.
LIST | Lists registered cards/names.
ADD <UID> <Name> | Registers or updates a card UID/name.
Example format
ADD 04:A1:B2:C3 Student One Replace the example UID with the exact UID printed after a real card scan.
Time limitation
The code logs elapsed uptime (millis), not a calendar date/time. An RTC or synchronized time source would be needed for real timestamps.

## Slide 9
Prototype Photos
The pictures document the physical assembly
9
View 1
Alternate views

## Slide 10
Testing & Results
All functional tests completed successfully on the assembled prototype
10
Assembly
Completed prototype assembled and documented in photographs.
Compilation & upload
Firmware compiled and uploaded to the ESP32 successfully.
LCD display
Startup message and “Scan your card” prompt displayed correctly.
RFID card tests passed
Registered card: attendance marked and student name displayed. Unregistered card: “Not registered”. Repeat scan: “Already marked”; no duplicate attendance during the current session.
Indicators & Serial output
Green LED and success beep confirmed accepted cards; red LED and error beeps flagged unregistered cards. Serial Monitor displayed card UIDs and attendance events.

## Slide 11
CONCLUSION
The RFID attendance workflow was implemented and tested successfully.
The source code supports UID registration, student-name lookup, LCD status messages, LED/buzzer feedback, session duplicate checking, and serial logging.
Result: all functional tests in the implemented project scope passed successfully.
Smart Attendance System Using RFID | Major Project